Arduino with ROS
LIST OF PROGRAMS:
1. Led Blink Built in.
2. LED Blink Separate on Bread Board.
3. Key Board Interface
4. LCD Interface.
5. Water Sensor Interface.
6. IR sensor Interface.
7. Push Button Interface.
8. Hellow World Code.
9. Speaker Interface.

        Install ROS Library in Arduino IDE:

Installing Arduino in ubuntu through terminal so that arduino link with ROS by using following commands:
INSTALL:
   sudo apt-get install ros-indigo-rosserial-arduino
   sudo apt-get install ros-indigo-rosserial
       INSTALL CATKIN WS:
  cd <ws>/src
  git clone https://github.com/ros-drivers/rosserial.git
  cd <ws>
  catkin_make
  catkin_make install
INSTALL ROS LIB:
  cd <sketchbook>/libraries
   rm -rf ros_lib
  rosrun rosserial_arduino make_libraries.py
     INSTALL ARDUINO LIB:
  cd <some_empty_directory>
 rosrun rosserial_arduino make_libraries.py

PROGRAMS:

Before each code run these 4 commands on separate terminals:

1. sudo arduino
2. rosrun rosserial arduino serial_node.py _ port:=/dev/ttyACM0
3. sudo chmod a+rw/dev/ttyACM0
4. rostopic echo chatterroscore

1 # LED BLINK:

#include <ros.h>
#include <std_msgs/Empty.h>

ros::NodeHandle nh;

void messageCb( const std_msgs::Empty& toggle_msg){
  digitalWrite(13, HIGH-digitalRead(13)); // blink the led
}

ros::Subscriber<std_msgs::Empty> sub("toggle_led", &messageCb );

void setup()
{
  pinMode(13, OUTPUT);
  nh.initNode();
  nh.subscribe(sub);
}

void loop()
{
  nh.spinOnce();
  delay(1000);
}

2 # LCD INTERFACE:

/*
 * rosserial Publisher Example
 * Prints "hello world!"
 */

#include <LiquidCrystal.h>
LiquidCrystal lcd(12, 11, 5, 4, 3, 2);

#include <ros.h>
#include <std_msgs/String.h>

ros::NodeHandle nh;

std_msgs::String str_msg;
ros::Publisher chatter("chatter", &str_msg);

char hello[13] = "Swarm RL";

void setup()
{
  lcd.begin(16, 2);

  nh.initNode();
  nh.advertise(chatter);
}

void loop()
{
  str_msg.data = hello;
  chatter.publish( &str_msg );
  nh.spinOnce();
  delay(1000);

  lcd.setCursor(0, 0);
  lcd.print(hello);
  delay(1000);
  lcd.clear();

}

3 # PUSH BUTTON:

/*
 * Button Example for Rosserial
 */

#include <ros.h>
#include <std_msgs/Bool.h>

ros::NodeHandle nh;

std_msgs::Bool pushed_msg;
ros::Publisher pub_button("pushed", &pushed_msg);

const int button_pin = 7;
const int led_pin = 13;

bool last_reading;
long last_debounce_time=0;
long debounce_delay=50;
bool published = true;

void setup()
{
  nh.initNode();
  nh.advertise(pub_button);

  //initialize an LED output pin
  //and a input pin for our push button
  pinMode(led_pin, OUTPUT);
  pinMode(button_pin, INPUT);

  //Enable the pullup resistor on the button
  digitalWrite(button_pin, HIGH);

  //The button is a normally button
  last_reading = ! digitalRead(button_pin);

}

void loop()
{

  bool reading = ! digitalRead(button_pin);

  if (last_reading!= reading){
      last_debounce_time = millis();
      published = false;
  }
  +
  //if the button value has not changed during the debounce delay
  // we know it is stable
  if ( !published && (millis() - last_debounce_time) > debounce_delay) {
    digitalWrite(led_pin, reading);
    pushed_msg.data = reading;
    pub_button.publish(&pushed_msg);
    published = true;
  }

  last_reading = reading;

  nh.spinOnce();
}

4 # BLINK LED:

#include <ros.h>
#include <std_msgs/Empty.h>

ros::NodeHandle nh;

void messageCb( const std_msgs::Empty& toggle_msg){
  digitalWrite(13, HIGH-digitalRead(13)); // blink the led
}

ros::Subscriber<std_msgs::Empty> sub("toggle_led", &messageCb );

void setup()
{
  pinMode(13, OUTPUT);
  nh.initNode();
  nh.subscribe(sub);
}

void loop()
{
  nh.spinOnce();
  delay(1);
}

5 # KEYBOARD INTERFACE:

#include <LiquidCrystal.h>
LiquidCrystal lcd(12, 11, 5, 4, 3, 2);

int ledpin =13;

void setup() {
  // put your setup code here, to run once:
  lcd.begin(16, 2);

Serial.begin(9600);
pinMode (ledpin, OUTPUT);

}

void loop() {
  // put your main code here, to run repeatedly:

while (Serial.available()==0);

int val = Serial.read();
char dis = char(val);
Serial.println(dis);

 lcd.setCursor(0, 0);
  lcd.print(dis);
  delay(5000);
  lcd.clear();

}

6 # SPEAKER:

// Pin to which an 8 Ohm speaker is connected (use a 150 - 220 Ohm resistor)
#define speakerPin 12

// Tempo (beats per minute)
#define bpm 96

// Gap between notes. This is expressed as percentage of time between 2 beats.
#define noteGapPercentage 10

/*
 * 2D array containing the notes to be played
 * A note comprises of two values:
 * * The first value determines the frequency of the note.
 * This is expressed as the number of a key on an 88-key piano (1 - 88)
 * A number outside this range can be used (e.g. 0) to create a gap
 * * The second value determines the duration:
 * * 1 represents a whole note (spans 4 beats)
 * * 2 represents a half note (spans 2 beats)
 * * 4 represents a quarter note (spans 1 beat)
 * * 8 represents an eighth note (spans 0.5 beat)
 * etc.
 */
uint8_t notes[][2] = {
  {35,4}, {35,4}, {42,4}, {42,4}, {44,4}, {44,4}, {42,2},
  {40,4}, {40,4}, {39,4}, {39,4}, {37,4}, {37,4}, {35,2},
  {42,4}, {42,4}, {40,4}, {40,4}, {39,4}, {39,4}, {37,2},
  {42,4}, {42,4}, {40,4}, {40,4}, {39,4}, {39,4}, {37,2},
  {35,4}, {35,4}, {42,4}, {42,4}, {44,4}, {44,4}, {42,2},
  {40,4}, {40,4}, {39,4}, {39,4}, {37,4}, {37,4}, {35,2}
};

// Time between two beats in microseconds (equal to length of a quarter note)
#define beatDuration (60.0 / bpm) * 1000000L

// Time of the gap between two notes in microseconds
#define noteGap beatDuration * (noteGapPercentage / 100.0)

void setup() {
  // Set the speakerPin as an output
  pinMode(speakerPin, OUTPUT);

  // Iterate over the notes array
  for(int i = 0; i < (sizeof(notes) / sizeof(*notes)); i++) {
    // pass the key number and note type
    playNote(notes[i][0], notes[i][1]);
  }
}

/*
 * Plays an individual note.
 *
 * keyNumber - The key number (1 - 88)
 * noteType - The note type (1, 2, 4, 8, etc.)
 */
void playNote(uint8_t keyNumber, uint8_t noteType) {
  long halfPeriod = getPeriodForKey(keyNumber) / 2;
  long noteDuration = beatDuration * (4.0 / noteType);
  long elapsed = 0;

  // While we have a note to play
  while(halfPeriod > 0 && elapsed < (noteDuration - noteGap)) {
    // Set speakerPin high for half of the period
    digitalWrite(speakerPin, HIGH);
    wait(halfPeriod);

    // Set speakerPin low for half of the period
    digitalWrite(speakerPin, LOW);
    wait(halfPeriod);

    // Update the amount of time that has elapsed
    elapsed += halfPeriod * 2;
  }

  /*
   * Gap between notes. Calculated using 'elapsed' to minimise timing errors
   * and ensure that the correct gap occurs whenever getPeriodForKey() returns
   * zero.
   */
  wait(noteDuration - elapsed);
}

/*
 * Returns the period for a key or zero for key numbers outside the range of 1 -
 * 88.
 *
 * keyNumber - The key number (1 - 88)
 */
long getPeriodForKey(uint8_t keyNumber) {
  // If the key is between 1 and 88
  if(keyNumber >= 1 && keyNumber <= 88) {
    // Return the period (one second divided by the frequency of the key)
    return 1000000L / (pow(2.0, (keyNumber - 49.0) / 12.0) * 440.0);
  }

  // Otherwise return zero
  return 0;
}

/*
 * Delay for a number of microseconds. This is necessary because
 * delayMicroseconds() has an upper limit.
 *
 * us - The delay in microseconds
 */
void wait(long us) {
  // First delay for the number of whole milliseconds using delay()
  delay(us / 1000);
  // Then delay for the remainder of microseconds using delayMicroseconds()
  delayMicroseconds(us % 1000);
}

void loop() {
  // Not used. Music will play once.
}

7 # HELLOW WORLD:

/*
 * rosserial Publisher Example
 * Prints "hello world!"
 */

#include <ros.h>
#include <std_msgs/String.h>

ros::NodeHandle nh;

std_msgs::String str_msg;
ros::Publisher chatter("chatter", &str_msg);

char hello[13] = "hello world!";

void setup()
{
  nh.initNode();
  nh.advertise(chatter);
}

void loop()
{
  str_msg.data = hello;
  chatter.publish( &str_msg );
  nh.spinOnce();
  delay(1000);
}

8 # WATER SENSOR:

#include "LiquidCrystal.h"
LiquidCrystal lcd(12, 11, 5, 4, 3, 2);

#define Water_detector 8
#define LED 9

void setup()
{ pinMode(Water_detector, INPUT);
   pinMode(LED, OUTPUT);
   Serial.begin(9600);
   lcd.begin(16, 2);

}
void loop()
{ if( digitalRead(Water_detector) == LOW)
   { Serial.println("No water");
       lcd.print("No Water");
       digitalWrite(LED,LOW);
   }
   else
   { Serial.println("Water");
       lcd.print("Water");
       digitalWrite(LED,HIGH);
   }

   lcd.clear();

}

9 # IR SENSOR INTERFACING:
#include <ros.h>
#include <ros/time.h>
#include <sensor_msgs/Range.h>

ros::NodeHandle nh;
sensor_msgs::Range range_msg;
ros::Publisher pub_range( "range_data", &range_msg);

#include <LiquidCrystal.h>
LiquidCrystal lcd(9,8,7,6,5,4);
const int analog_pin = 0;

float getRange(int pin_num)
{ int sample = analogRead(pin_num);

    Serial.println(sample);
    lcd.print( sample );
    delay(100);
    lcd.clear();
    return (sample); }
void setup()
{ nh.initNode();
   nh.advertise(pub_range);

   lcd.begin(16, 2);
   lcd.setCursor(0, 0);
   Serial.begin(9600); }
void loop()
{ range_msg.range = getRange(analog_pin);
    pub_range.publish(&range_msg);
    nh.spinOnce();

        }

10 #